## Slide 1: Data Linking Subcommittee
Annual Conference 2022

## Slide 2: Agenda
Agenda check
Harvest tracking proof of concept
2022 WGs Recap
  In-field Product ID
  DatasetMetadata
  Traceability API
Driving Implementation
WG Roadmap for 2023

## Slide 3: 2022 Grain Traceability Pilot
Development of Implementation Guidelines

## Slide 4: Pilot Objectives
Develop the concepts and definitions of core traceability components:
  CTE, Critical Tracking Events,
  TRU, Traceable Resource Units
Develop implementations of the concepts applied to the Use Case of traceability of bulk commodity grains specifically corn and soybeans
Develop and test concepts for TRU management for this use case
Develop use cases to test metadata and Open API standards being developed to facilitate the discovery of relevant data contained in third party data repositories:
  Combine yield monitor data
  Grain cart load cell data
Develop specifications for Open API standards for the retrieval of specific data elements from these repositories

## Slide 5: Harvesting System Used in Pilot

## Slide 6: Pilot System Requirements
Mobile Device
  Create CTEs for all transfer events,
  Create and manage active TRUs for all containers/vehicles
  Record relevant key data elements and attach to appropriate TRU
System Server
  Maintain a repository of all containers used in the harvest
  Maintain a real time “state” of each container,
  Maintain an log of key events for each container in the system
  Implement API(s) for interaction with:
    Other “linked” systems
      Containers
      Linking TRUs
    Data repositories containing key data elements

## Slide 7: TRU Management Rules
Each container will be associated to multiple TRUs during a harvest season
At any time a container will be associated with only one TRU (active TRU)
Each container is responsible for its TRU management
  Defining new TRUs
  Publishing its current active TRU to the rest of the harvesting system

## Slide 8: Implementation Hardware
Mobile Devices
  Android Tablet – Samsung Active3 (1)
  Android Phone – Samsung S10 (2)
  Specs:
    GPS
    SQL Lite db
Server
  AWS Serverless
    Postgress db
  AWS Gateway API
  Lambda functions (Python v3.7)

## Slide 9: Pilot Results

## Slide 10: Pilot Results (con’t)
485 total Transfer CTE’s
  Field->Combine – 191
  Combine->Grain Cart – 179
  Grain Cart -> Semi - 66
  Semi -> Storage Unit - 41

## Slide 11: Visualization Challenge

## Slide 12: Lessons Learned

## Slide 13: Transfer CTE Fundamentals
Time Scope
  Start
  Stop
Containers
  Source
  Target
Active TRUs
  Source
  Target
Material
  Type
  Quantity

## Slide 14: Container Proximity Detection
Technologies
  IoT – Bluetooth
  WIFI SSID
  Geo-location
  BarCode
Lessons Learned/Guidelines
  For fixed assets geo-location is the clear winner
  WIFI SSID has the advantage of broad implementation
  IoT Bluetooth requires programmable device for each container
  None are 100% effective

## Slide 15: Data Linking API
Data Linking
  Leverage Dataset metadata; need OEM and FMIS to use it
  Open API Standards
  Base URL and End Points
  Device ID provided by OEM
  Access/permission token
  Requested data identifier (ex. ISO11783 DDI)
  Time Scope

## Slide 16: TRU Linking
Seafood Traceability SYSTEMS: GAP Analysis OF Inconsistencies IN Standards AND NORMS
  https://pdf4pro.com/view/seafood-traceability-systems-gap-analysis-of-357b04.html
Internal
  Internal traceability is the traceability within a link or a company
Chain
  Chain traceability is the traceability between links and companies, and it depends on the data recorded in the internal traceability system being transmitted, and then read and understood in the next link in the chain
  Trading partners must agree on how to identify the TUs and then send the required information through another channel (fax, mail, through electronically integrated systems) while referring to the TU in question.

## Slide 17: TRU Linking
Purpose
  Transfer CTE define transfers between source and target containers AND their respective “active TRUs”
Types
  Linking “within system” CTEs
  Linking “across systems” CTEs
API Parameters
  Access/Permissions token
  ContainerID
  Time Scope

## Slide 18: Implementation Technical Issues
Referential Integrity
  Containers
  Active TRUs
Redundant points in “crumb trail” WKT linestrings
  For Oct. 19 data
    291,000 ->9300 with a simple generalization algorithm
Time Synchronization

## Slide 19: Opportunities for Innovation
Automated “Data Linking” and retrieval
  Dataset Metadata standards,
  OpenAPI standards for linking and retrieval
Mobile Device - CAN Interface
  Use CAN messages to replace “button push”
OEM Integration
  Replace mobile device
  Requirements:
    Shared Container Repository
    TRU Management Algorithms
    Simple proximity detection over-ride UI
Material Flow Modeling
  Harvest - “On-The-Go” unloading
  Planting -

## Slide 20: WG20 Traceability API Project Overview
Recap

## Slide 21: API track
Leverage prior work
  CART
  KSU / TSU ontology research
  Dataset Metadata
  Years of discussion
Model TRU, CTE and related components in Score
Use components to build OpenAPI definition
Enable service providers share datasets using Dataset Metadata integration from which CTEs and TRUs can be elicited using processing algorithms

## Slide 22
Traceability Repo
(discovered
CTEs, TRUs)
Traceability API ideas for client:
GET /tru-list?kde.id=$&kde.type
GET /cte-list?kde.id=$&kde.type
API Client
Dataset metadata driven integration
Notes: The OEM Platform alone is not enough to solve the transfer event discovery, that all datasets and event messages needed to be merged together to truly identify the transfer event. With integration via the recently released Dataset Metadata, data can be more easily shared to traceability repositories where TRU and CTE discovery can take place, and an API can be provided for future root cause analysis.

## Slide 23: Dataset Metadata
Agricultural Use Cases for Data Linking

## Slide 24: Background

## Slide 25: Precision Agricultural
ISO 11783 extends ISO 11898 Controller Area Network standard
Large datasets generated while performing field operations
Farmers own mixed fleets
Tractor displays don’t last forever; retrofits available
Different Cloud platforms

## Slide 26: Mixed Fleets

## Slide 27: Supply Chain pressures
Supply chain pressures to trace premium commodities
  More direct ship to processor from field
  Field to fork traceability
  Accurate inventory management of commodities
Food origin, quality, and safety concerns increasing
  Consumer Demand (gluten-free, non-GMO)
  Product Recall (listeria, e-coli, etc.)

## Slide 28: Agricultural Lifecycle
Soil Health
As-Applied
As-Harvested
As-Planted
Weather
Supply Chain
Equipment
Manufacturers
Technology
Providers
Agronomy
Services
Testing
Services
Crop Nutrient Manufacturers
Food
Processors
Consumer
Retail
Crop Protection Manufacturers
Co-op Retail / Elevators
Seed Manufacturers
Animal Nutrition Services
Exploded view

## Slide 29: State of Precision Ag
Some improvements of equipment capabilities
OEM and FMIS Platforms moving to proprietary OpenAPIs
AgGateway ADAPT frameworks has provided better data translation capabilities, interoperability
Still limited capabilities to capture product information in the tractor display and related data (lot, shipment id)
Hard for farmers to share data across platforms

## Slide 30: Product driven approach

## Slide 31: Closed Loop Approach
Manufacturer
Distributor
Retailer
Field Operator
Farmer
Product Catalog
Agronomic
R&D Product Spec
Packaging
Warehouse Locations
Manufacturing Batch/ Lot
E-Commerce
Shipments with Lot/Batch
Agronomic Recommendations
Sales
Shipments with Lot/Batch
Planning
Receipts with Lot/ Batch
Finance
Assets
Asset Utilization
Work Order
Product Identification with Lot /Batch
Work Record Datasets (CN, Seed, CP, Harvesting)

## Slide 32: Product Centric View
Co-operative/ Distributor
ShippedIemInstance API
Tractor Display
Retailer Systems
Catalog API
Reference Data API
FMIS
Product Setup
Orders
Shipments
POST /plantingworkorder
GET
/setupfiles
GET
/shippediteminstance
POST
/shippediteminstance
GET
/catalog
GET
/catalog
Manufacturer
OEM Platform
Raw Datasets
Improving the quality of our raw work record datasets starts with accurate product information

## Slide 33: Data linking

## Slide 34: Different types of Linked Data
Datasets –‘big data’ from logged field operations work records
CAN messages
Weather conditions
Soil health test results
Business Transactions leading up to these operations
Data itself is NOT sufficient to link – need metadata about the data

## Slide 35: ‘Simple’ Harvesting Use Case
Combine grain auger – on/off
Harvest yield data
Grain cart auger – on/off
Grain cart weights
IoT proximity sensors

## Slide 36
Semi Trailer
Co-op Grain Elevator
On-Farm Storage
Semi Trailer
Seed Manufacturing
Distribution
Retailer Sales
Grower Receipt
Planting
Crop Protection
Crop Protection
Manufacturing
Crop Nutrition
Mix (MixTicket)
Harvest
Semi Trailer
Retailer/Elevator Receipt
Crop Nutrition
Application
The ‘Perfect’ Storm
Weather
Soil
Processor
Receipt
Notes: What are the arrows depicting? Reference links?

## Slide 37: Dataset metadata

## Slide 38: Our Approach: 3+ years of work
FAIR Principles
Dublin Core
W3C DCAT
Dataset Metadata

## Slide 39: FAIR Principles
Findable – Key Data Elements, Text to help search and match
Accessible – Security, Who to contact, Retrievable
Inter-operable – understand the format of the data
Reusable – richly described to articulate its value
https://www.go-fair.org/fair-principles/

## Slide 42: GitHub Review
Schema
Example for processed data

## Slide 43: Use cases

## Slide 44
Improvements to Business Processes
Since we know planting records…
No need to identify product during tissue sampling
No need to identify product during harvest operations
Better inventory management including segregation of premium commodities

## Slide 45: Sharing of Datasets Farmer needs a consistent experience
Raw
Processed
Summary

## Slide 46: Findable
Product recall, locate origin of aflatoxin
Federated search across several Cloud Platforms
Peer-to-Peer

## Slide 47: Driving Implementation
Next steps for completed Digital Resources

## Slide 48: Agrisemantics
Process for identifying, submitting, updating controlled vocabularies

## Slide 49: Agrisemantics Submission

## Slide 50: Future Working Groups